Sixty Four Pixels / For full build instructions and step-by-step guides, please check out https://github.com/hotchk155/AVRGame/wiki / Your kit includes: / Printed circuit board / IC1, IC2 - TPIC6B595N power logic shift register / IC3 - ATMEGA328P-PU microcontroller / R1-R8 - 220R resistor (red-red-black code) / R9 - 1K resistor (brown-black-red code) / C1, C2 - 33pF ceramic capacitor (33 code) / C3, C4, C5, C6 - 100nF cap (104 code) / X1 - 16MHz crystal / PWR - Miniature slide switch / LED1 - 3MM standard LED. The longer leg is the anode (+ terminal) / SPK1 - 5V piezo transducer. The anode (+ terminal) is identified on the label. Remove the label after fitting. / A,B,C,D,RESET - 6mm tactile switch / SERIAL - 6 pin male header 0.1" pitch. This is intended to fit a standard FTDI USB-to-TTL serial programming cable (not supplied) / DISP1 - 8x8 red/green LED matrix. Pin 1 is indicated with a coloured label. Please ensure correct fitting to the board – it is very difficult to remove if soldered incorrectly! / IC sockets (20 and 28 pin). Line up the notch on the end with the image on the board / 3xAAA battery box with flying leads. Trim leads to required length. Please see web site for advice / Double sided foam pads to fix battery box to reverse of PCB. These need to be cut to fit. Please see web site for advice. / To contact me, please email sixtyfourpixels@gmail.com

Sixty Four Pixels / For full build instructions and step-by-step guides, please check out https://github.com/hotchk155/AVRGame/wiki / Your kit includes: / Printed circuit board / IC1, IC2 - TPIC6B595N power logic shift register / IC3 - ATMEGA328P-PU microcontroller / R1-R8 - 220R resistor (red-red-black code) / R9 - 1K resistor (brown-black-red code) / C1, C2 - 33pF ceramic capacitor (33 code) / C3, C4, C5, C6 - 100nF cap (104 code) / X1 - 16MHz crystal / PWR - Miniature slide switch / LED1 - 3MM standard LED. The longer leg is the anode (+ terminal) / SPK1 - 5V piezo transducer. The anode (+ terminal) is identified on the label. Remove the label after fitting. / A,B,C,D,RESET - 6mm tactile switch / SERIAL - 6 pin male header 0.1" pitch. This is intended to fit a standard FTDI USB-to-TTL serial programming cable (not supplied) / DISP1 - 8x8 red/green LED matrix. Pin 1 is indicated with a coloured label. Please ensure correct fitting to the board – it is very difficult to remove if soldered incorrectly! / IC sockets (20 and 28 pin). Line up the notch on the end with the image on the board / 3xAAA battery box with flying leads. Trim leads to required length. Please see web site for advice / Double sided foam pads to fix battery box to reverse of PCB. These need to be cut to fit. Please see web site for advice. / To contact me, please email sixtyfourpixels@gmail.com